## Slide 1
认知网络
Cognitive Network
汇报人：巫锐
组员：郭雨轩 邓经纬

## Slide 2
目录
CONTENTS
1
认知网络的产生背景
2
认知网络的结构
3
认知网络的发展过程
4
基于机器学习的认知网络

## Slide 3
认知网络的产生背景
01

## Slide 4
20世纪九十年代，随着无线通信技术的飞速发展，频谱资源变得越来越紧张。为保护频谱资源，管理部门将特定的授权频段以供特定通信业务使用。频谱被分为授权频段及非授权频段。非授权频道频谱资源远少于授权频道，但由于管理困难，频谱利用率非常低。为了提高频谱利用率，具有认知功能的无线通信设备可以按照某种“伺机”的方式工作在已授权的频段内，即非授权通信用户通过“借用”的方式使用已授权的频谱资源（通信不会影响到其他已授权用户的通信）。
认知无线电是认知网络的前身，如今二者是包含关系。
一、产生背景——认知无线电
Notes: 认知无线电的目的是解决频谱紧张问题。

## Slide 5
网络系统的结构复杂性、环境复杂性、需求复杂性急剧增长
随着计算机技术及互联网的普及
网络系统管理愈加困难，网络元素（节点、协议、策略、行为等）缺乏智能的自适应能力，因此整体网络性能及端到端系统性能得不到保障
网络系统管理困难
开发一种具有“学习”能力的网络结构，使其具有自适应结构，可以对网络环境进行感知、规划、决策、行动、学习、策略。
启发
一、产生背景
Notes: 近年来，随着人们经济水平和生活质量的提高，互联网也走入了家家户户，人们对网络的需求的多样性使网络结构复杂性、环境复杂性和需求复杂性急剧增长。导致网络系统管理愈加困难，网络元素（节点、协议、策略、行为等）缺乏智能的自适应能力，因此整体网络性能及端到端系统性能得不到保障。而什么样的结构可以实现类似功能呢，科学家们想到了自认知无线电。

## Slide 6
认知网络定义：
指网络能够感知外部坏境，通过对外部环境的理解与学习，实时调整通信的内部配置，智能地适应外部环境的变化。
一、产生背景
“学习”的能力：
考虑通信环境中的每一个可能参数，然后做出决定。
机器+学习=机器学习
Notes: 计算机网络，电力网络都是机器网络。机器+学习=机器学习

## Slide 7
认知网络的结构
02

## Slide 8
传统认知网络的设计结构：
Notes: 讲解结构的交互流程

## Slide 9
二、认知网络的结构
关键词：SAN –a type of SDN
Software-defined networking (SDN) technology is an approach to network management that enables dynamic, programmatically efficient network configuration in order to improve network performance and monitoring, making it more like cloud computing than traditional network management.
Notes: A for adaptation

## Slide 10
二、认知网络的结构
This paper proposes an approach to network design based on tools from AI and cognitive systems. Specifically, we propose a construct, a distributed cognitive system that permeates the network, that we call the knowledge plane.
from: A Knowledge Plane for the Internet
Notes: knowledge plane的提出在mit计算机学院教授的一篇论文

## Slide 11
认知网络的发展
03

## Slide 12
二、认知网络的发展
FOCALE认知模型

## Slide 13
二、认知网络的发展
self-net认知模型:
An approach for designing cognitive self-managed Future Internet
Notes: 欧洲

## Slide 14
二、认知网络的发展
self-net认知模型:
The Self-NET project is a European research project part of the Future Internet and Research (FIRE) projects initiative, which investigates, designs and prototypes aspects for envisaged Future Internet networks by adding the dimension and potential of applied self-management and use of cognitive functionalities in such networks building on the principles of autonomic network management.

## Slide 15
传统认知网络的设计结构：
Notes: 讲解结构的交互流程

## Slide 16
二、认知网络的发展 – 关键技术总结
知识表示
学习和推理
网络重配置
环境上下文感知
跨层设计

## Slide 17
可能的实现方案
多代理技术
标准代理技术
智能代理具备特征
智能性
反应性
学习性
协作性

## Slide 18
机器学习&认知网络
04

## Slide 19
Why ML
low cost
energy, computing resource
one for all
easily adapt to different network conditions
automatic learning
meets the need of adaptation

## Slide 20
深度强化学习 Deep Reinforcement Learning
深度强化学习以一种通用的形式将深度学习的感知能力与强化学习的决策能力相结合,并能够通过端对端的学习方式实现从原始输入到输出的直接控制。

## Slide 21
Deep Reinforcement Learning 深度强化学习
combines reinforcement learning (RL) and deep learning (DL).
RL considers the problem of a computational agent learning to make decisions by trial and error.
DL allows agents to make decisions from unstructured input data without manual engineering of the state space.

## Slide 22
Advantages of DRL
Energy-saving
In this paper, the proposed DRL-based framework solves the green resource allocation problem in mobile edge networks. A well-trained network achieves not only the aim of green energy-saving, but also solve the problem of resource allocation.
--conclusion of Deep Reinforcement Learning based Green Resource Allocation Mechanism in Edge Computing driven Power Internet of Things
Notes: paper of BUPT

## Slide 23
Advantages of DRL
fits large-scale model
(Reinforcement Learning) perform poorly for large-scale models, DRL combines deep neural network with Q-learning, referred to as Deep Q-Network (DQN), for overcoming this issue.
cognitive networks consider mainly large-scale networks
Notes: actual networks are large-scale models

## Slide 24
Advantages of DRL
unsupervised
Don’t require prior knowledge about the system model
for cognitive networks:
classify x
find the best configuration √
category of

## Slide 25
we replicated a research: Deep Multi-User Reinforcement Learning for Dynamic Spectrum Access in Multichannel Wireless Networks
Purpose
Network Model
Algorithms
Deficiency

## Slide 26
Purpose: What’s the users’ demand?
The goal of the users is to maximize a certain network utility in a distributed manner without online coordination or exchanging messages used for managing the spectrum access.

## Slide 27
Purpose: explain the demand
The goal of the users is to maximize a certain network utility in a distributed devices: mobile phones, laptops, …
without online coordination or exchanging messages:
Do you want your mobile phone to exchange messages all the time in a wireless network?

## Slide 28
Purpose
To meet the users’ needs:
develop a distributed learning algorithm for dynamic spectrum access that can effectively adapt for general complex real-world settings.

## Slide 29
Purpose
corresponding the architecture introduced before:
another advantage of ML:
conceal the complex cognition process

## Slide 30
Network Model
We consider a wireless network consisting of a set 𝒩 = {1, 2, ..., 𝑁} of users and a set 𝒦 = {1, 2, ..., 𝐾} of shared orthogonal channels.
At each time slot, each user is allowed to choose a single channel for transmission with a certain attempt probability (i.e., Aloha type narrowband transmission). We assume that users are backlogged, all users always have packets to transmit.
Notes: orthogonal 正交

## Slide 31
Algorithms
The algorithm was originally designed using Deep Q-Learning for a single agent who interacts with a fully observable Markovian environment and demonstrated strong performance when handling more involved settings (e.g., multi-agent, non-Markovian environment).
from a simple model to complex ones

## Slide 32
Data
result of the source code of the research:
DRL versus Slotted Aloha (a popular wireless network protocol)
after dozens of time slots’ training, channel utilization exceeds Slotted Aloha greatly

## Slide 33
Data: found further work to improve productivity
Related source code from https://github.com/shkrwnd/Deep-Reinforcement-Learning-for-Dynamic-Spectrum-Access:
We implemented DRL on this problem to get efficient throughput and to reduce the collisions on network. Convergence period of this method increases with number of users and it becomes impractical to use. It works optimum and useful for few users and channels. Therefore we break network into small clusters which are optimized first then the nodes above in bottom up approach.
using TensorFlow to implement distributed computation to improve productivity

## Slide 34
Data
one only agent
(12 users and 8 channels)
comparing with
distributed agents
(4 clusters of 3 users and 2 channels)
result of some extra work on GitHub: https://github.com/shkrwnd/Deep-Reinforcement-Learning-for-Dynamic-Spectrum-Access
Notes: more likely to get higher reward, which means better training results

## Slide 35
Deficiency of the research
the model is too simple
needs to be trained frequently when the state changes
Notes: although the algorithm can be generalized, it seems need to be completely renew when new users come…

## Slide 36
分工
郭雨轩：认知网络基本概念和设计结构部分资料收集、ppt制作
邓经纬：DRL的概念及ML在认知网络中的应用资料收集
巫锐：展示内容设计和分工，关键技术分析，相关研究复现，ppt制作